## Slide 1
Preprocessing Steps: These steps can be done prior to the algorithm calculation loop beginning.
PS1-Data input
from BY CAMD Hourly File
PS1.04-Create the 3 hourly hierarchies (hourly, 6-hour, 24-hour) from CAMD generation data for each region and ERTAC Fuel/Unit Type Bin
PS1.02-Run edit checks on the information in the BY CAMD hourly file
PS1.07-For each hour of the year in each ERTAC Fuel/Unit Type Bin, calculate the BYGen, BYRetGen, FYGen and FYGrowth
PS1.05-For partial year reporters, create hourly BY records using annual HI data and a default temporal profile for hours not reported to CAMD
PS1.03-Create report on units with data outliers
PS1.08-For each ERTAC_region and ERTAC_fuel/unit type bin, determine the unit allocation order.
PS1.01-Remove data for units designated as non-EGUs by States/MJOs
ID of non-EGU CAMD units is made thru State database inputs.
Data from PS2.01 also needed.
Data from UAF or EGrid needed for annual HI.
Data also needed from PS3.01 and UAF.
UF data and new unit data from the UAF needed.
PS1.09-Output a unit allocation file and an hourly hierarchy file suitable for import into the algorithm to allow States to review and update the information
PS1.06-Create report on partial year units.
The temporal profile for the unreported months is a flat line, with even distribution of activity..

## Slide 2
2
PS2.07-Run edit checks on the information in the UAF
PS2.04-For each existing and new unit in the UAF, calculate the hourly Optimal Load Threshold using the percentile of the hourly data as described in the Input Variables worksheet.
PS2.05-For each existing and new unit in the UAF, calculate the max_annual_ ERTAC_UF.
PS2.03-Determine the max_ERTAC _heat_ input_ hourly_summer for each existing and new unit in the UAF.
PS2.01-For every unit in the UAF, determine the ERTAC Fuel/Unit Type Bin
PS2.02-For each existing and new unit in the UAF, calculate the ERTAC Heat Rate (annual average)
PS2.06-For new units in the UAF, calculate the hourly proxy generation
PS2.09-Output a UAF and hourly proxy listing suitable for import into the algorithm to allow States to review and update UAF information
PS2-Data input
from the Unit Availability File (UAF)
Use data in the BY CAMD Hourly File
Use data in the BY CAMD Hourly File
Use data in the BY CAMD Hourly File
The outputs of this function won’t be put into the UAF. They will be put in a separate, hourly file.
PS2.08-Create report on units with data outliers
Preprocessing Steps: These steps can be done prior to the algorithm calculation loop beginning.

## Slide 3
PS3.01-Calculate the non-peak hourly growth rates and the hour specific growth rates as a function of the annual growth factor, the peak growth factor, and the transition hours for each region and ERTAC Fuel/Unit Type Bin and hour of the year
PS3-Data input
from the Growth File
Preprocessing Steps: These steps can be done prior to the algorithm calculation loop beginning.

## Slide 4
Beginning of projection tool: Deficit check and creation of generation deficit units, if needed. New units inserted into the hierarchy. Run by fuel/unit type and region. Order of regions run may be important for future iterations of the model, to try to account for regional energy transfers.
2-Begin at the first/next
hour in the hour-of-year hierarchy
3-For the specific hour, calculate:
TotalProxy, AFYGrowth,
AFYGR
3.5-hr = deficit
check?
3.5 Y- More generation capacity needed?
3.5Y.1-Add new generation deficit unit(s)
N
Y
Y
N
3.5Y.2- Insert generation deficit unit(s) in UAF and calculate unit data, including optimal load threshold, max_ annual_ERTAC_UF, & hourly proxy gen.
3.6-Re calculate the unit allocation order with the new generation deficit unit(s)
Begin at the first hour in the hierarchy
Next page: gener-ation assignment

## Slide 5
Draft-Version #19
5
5-Multiply the BY
operational input/output
of each existing unit by AFYGR
6-Has the
max capacity of
any unit
been reached?
4-Is the
AFYGR
‹1?
4Y.3-
Was this hr
8,760?
9N-Go to next hr (2)
7-Set the utilization of any
unit exceeding its capacity
back to the maximum allowed
8-Calculate ExGen pool for this hour:
Sum the amount of generation
for this hour that exceeded the
capacity of each unit
Y
Y
N
N
Y
4Y.2.a-Multiply the BY operational input/output of each unit by AFYGR
4Y.1-Raise a blue flag to indicate excess new capacity and document AFYGrowth
4Y.3.Y-Go
to next page: ExGen pool Dist
The comparison in 6 should be made to hourly and annual capacities and utilization fractions (UF).
4Y2-Assign proxy
generation to new units
4.5-Assign proxy generation to new units
4Y.3.N-Go to
next hr (2)
9-
Was this hr
8,760?
9Y-Go
to next page: ExGen pool Dist
N
Y
N
From previous page/ deficit check
Assignment of Generation/Excess Generation (ExGen) Pool Creation.

## Slide 6
11-For first unit in allocation listing,
allocate utilization of that unit
from the ExGenPool
12-Has the unit
optimal threshold
or any annual capacity
of that unit
been reached?
12N.2-Go to next hr (10.5)
N
Y
ExGen Pool Distribution: This routine is done for hours where there is an ExGen pool. Continues the generation allocation to units. If the option is included to estimate energy transfer between regions, this would be done for primary and secondary consuming regions.
12N-Has hr
8,760 been
reached?
12N.1-Go to
spinning reserve page
N
Y
The current setup distributes the ExGenPool in 2 passes as shown on next page. Future iterations may want to distribute the ExGenPool in up to 5 passes.
10-Previous page: ExGen pool creation
10.5-Begin at the first/next hour in the hour-of-year hierarchy
12Y-Go to next page: double loop distribution
At this point, the program has distributed every hour’s ExGenPool for every fuel unit type in a region and must begin the spinning reserve test.

## Slide 7
13-Go to next unit on
allocation hierarchy
14-Any
units
left?
14Y.1-Allot utilization to the next unit on the allocation listing
14Y.2-Has the unit optimal threshold or any annual capacity limit of the unit been rchd?
14Y.3-Has hr
8,760 been
rchd?
14Y.3N-
Go to
next
hr (10.5)
N
N
N
Y
Y
Y
14Y.3Y-Go to
spinning reserve test
15-For first unit in allocation listing, allocate utilization
of that unit from the ExGenPool
16-Has any max capacity of that unit been reached?
17-Go to next unit on
allocation hierarchy
18-Any
units
left?
18Y.1-Allot utilization to the next unit
on the allocation listing
N
16N.1-Hr 8760 been
rchd?
16N.1Y-Go to
spinning reserve test
N
Y
From 12Y:
Y
N
Y
ExGenPool Distribution: two loops

## Slide 8
Spinning Reserve: Checks to ensure that spinning reserve requirements for each region of the system are met. This portion of the work is performed after power distribution and ExGen pool distribution have been performed for all three fuels (coal, oil, natural gas). Spinning reserve for any hour can be satisfied by any extra capacity in any fuel type. The amount needed is calculated by finding the maximum capacity of the largest single unit running in any hour using any fuel and multiplying by 100%.
20-For each hour,
determine the capacity
of the largest unit operating
21-The required reserve capacity
equals 100% of the capacity
of the largest unit operating
23-Enough reserve
capacity exist in that hour?
22-Beginning at the first hour
in the hour of year hierarchy,
compare the required
reserve capacity to the
amount of generation in the system
not being used.
23Y-Hr 8760 rchd?
24-Go
to
next
hour
(23)
Y
N
N
Y
25-Go to
next page: Emissions Check
23N-Send up red flag : more cap needed
23Y1-Print out a useful report detailing all reserve capacity needed.
23.5Y1-Output a database of hourly generation/heat input data for each unit as well as a summary table of unit generation/heat input (base yr versus future yr)
19.5-Print out a useful generation report by unit for stakeholder review
19.1-If any hour showed a demand generation deficit, print out a useful report showing where, when, how much, and for new generic unit creation, data on those units.
19 From previous pages

## Slide 9
Emissions Check: This part of the work checks to see if the expected controls, new generation, future year generation, and other system changes allow the universe of units to meet the various environmental caps.
25-
From spinning reserve page
26-For each hour of the year, for each unit, calculate emissions of
NOx, SO2, and CO2(e).
27-For units subject
to the Transport
Rule, are all caps met?
N
26.5-Apply unit level controls for units where future retrofits are expected to occur, based on information provided by States in the Controls and Emissions file
27.5 Assign generic controls as described in the narrative to meet caps in the future year
X
27.5B-Send up a flag that more control was needed and print out a useful report detailing generic controls
Y
28-Print out a useful report for the SIPs and output a database (ORL, NIF, or similar) that can be used for AQ modeling purposes. Reports need significant detail to allow review of the results from application of transport and other state caps.
STOP Tool: Start the QA Process
The processes of decision #27 are described on Page 11
This portion of the programming was not completed.

## Slide 10
29-For units subject
to the Midwestern
Greenhouse Gas
Reduction Accord,
are all caps
met?
30-For units subject
to the Regional Greenhouse
Gas Initiative, are
all caps met?
30N-Send up
a flag for
more EE or
control
needed and
print out a
useful report
29N-Send up a flag for
more EE
or control
needed
and print out a useful
report
31-Stop and print out a useful report for those interested showing compliance/noncompliance with the climate change caps
N
N
Y
Y
27: From decision on meeting caps
GHG Cap Checks: Checks any GHG caps that are supplied and creates report on output.. This page is part of Decision #27 on the previous page.
Go to State Cap Check

## Slide 11
Decision 27 Explanation: This section checks to see if the emissions from the universe of EGUs may comply with the Transport Rule and other requ’ts. If state designated controls are not sufficient to demonstrate compliance with any particular cap, 27.5 assigns specific controls until rule requirements are met at state and/or group levels. 27.5 currently is not programmed, so this function does not work, as of yet.
27.1a- For each state, calculate annual NOx, annual SO2, and ozone season NOx in the future year.
27.1b-Compare each state’s future year emissions totals to the totals for OS NOx, Annual NOx, and Annual SO2 listed in the State Total Listing.
State totals could be assurance levels, budget levels from CSAPR, or other appropriate state budgets; only for states subject to a state cap requirement.
27.5B-Send up a flag that more control was needed and print out a useful report
N
27.5 Assign generic controls in the state(s) with excess emissions as described in the narrative to meet caps in the future year
27.1c-Is each state’s future emissions of SO2, annual NOx, and OS NOx less than or equal to the state cap?
Y
X
27.6-Go to next page: Group CAPs Check
State Cap Requirements
Does not current perform this function
From GHG Check

## Slide 12
27.1d-Is the regional group’s future emissions of SO2, annual NOx, and OS NOx less than or equal to the group cap? (multiple potential groups to check)
27.2a-Compare each group of state’s future year emissions totals to the applicable totals for that year for OS NOx, Annual NOx, and Annual SO2 listed in the Group Total Listing.
27.5 Assign generic controls in the regional group with excess emissions as described in the narrative to meet caps in the future year
27.5B-Send up a flag that more control was needed and print out a useful report detailing generic controls
28- Goes back to the emissions check page
N
Y
X
There are as many groups as need to be defined for each pollutant: annual SO2 and NOx, OS NOx. The listing must delineate both the group total emissions for each pollutant and the states included in each group.
27.6-From State Caps Check
Group Cap Check: Checks to see if regional caps are met, made up of state clusters.