## Slide 1
Preprocessing Steps: These steps can be done prior to the algorithm calculation loop beginning.
PS1-Data input
from BY CAMD & ERTAC Non-CAMD Hourly File
PS1.05-Create the 3 hourly hierarchies (hourly, 6-hour, 24-hour) from CAMD generation data for each region and ERTAC Fuel/Unit Type Bin
PS1.02-Run edit checks on the information in the BY CAMD hourly file
PS1.08-For each hour of the year in each ERTAC Fuel/Unit Type Bin, calculate the BYGen, BYRetGen, FYGen and FYGrowth and note any demand transfers
PS1.06-For partial year reporters, create hourly BY records using annual HI data and a default temporal profile for hours not reported to CAMD
PS1.03-Create report on units with data outliers
PS1.09-For each ERTAC_region and ERTAC_fuel/unit type bin, determine the unit allocation order.
ID of non-EGU CAMD units is made thru State database inputs.
Data from PS2.01 also needed.
Data from UAF or EGrid needed for annual HI.
Data also needed from PS3.01 and UAF.
UF data and new unit data from the UAF needed.
PS1.10-Output a unit allocation file and an hourly hierarchy file suitable for import into the algorithm to allow States to review and update the information
PS1.07-Create report on partial year units.
The temporal profile for the unreported months is a flat line, with even distribution of activity..
PS1.04-Convert seasonal controls to controls for specific FY
PS1.01-Remove data for units designated as non-EGUs by States/MJOs

## Slide 2
2
PS2.09-Run edit checks on the information in the UAF
PS2.06-For each existing and new unit in the UAF, calculate the hourly Optimal Load Threshold using the percentile of the hourly data as described in the Input Variables worksheet.
PS2.07-For each existing and new unit in the UAF, calculate the max_annual_ ERTAC_UF.
PS2.05-Determine the max_ERTAC _heat_ input_ hourly_summer for each existing and new unit in the UAF.
PS2.01-For every unit in the UAF, determine the ERTAC Fuel/Unit Type Bin
PS2.04-For each existing and new unit in the UAF, calculate the ERTAC Heat Rate (annual average)
PS2.08-For new units in the UAF, calculate the hourly proxy generation
PS2.11-Output a UAF and hourly proxy listing suitable for import into the algorithm to allow States to review and update UAF information
PS2-Data input
from the Unit Availability File (UAF)
Use data in the BY CAMD Hourly File
Use data in the BY CAMD Hourly File
Use data in the BY CAMD Hourly File
The outputs of this function won’t be put into the UAF. They will be put in a separate, hourly file.
PS2.10-Create report on units with data outliers
Preprocessing Steps: These steps can be done prior to the algorithm calculation loop beginning.
PS2.02-Calculate unit specific stats (e.g., OS heat rate)
PS2.03-Calculate base year operating hours

## Slide 3
PS3.01-Calculate the non-peak hourly growth rates and the hour specific growth rates as a function of the annual growth factor, the peak growth factor, and the transition hours for each region and ERTAC Fuel/Unit Type Bin and hour of the year
PS3-Data input
from the Growth File
Preprocessing Steps: These steps can be done prior to the algorithm calculation loop beginning.

## Slide 4
Beginning of projection tool: Assigning grown and proxy generation, while making note of times when grown generation cannot be allocated or excess generation might not be able to be allocated.
2-Begin at the first/next
hour in the hour-of-year hierarchy
3-For the specific hour, calculate:
TotalProxy, AFYGrowth,
AFYGR (considering demand transfers)
3.5-hr = deficit
check?
3.5aY- Need more capacity to cover proj. gen., incl. transfers?
N
Y
Y
N
Next page: add GDUs
4-Is the
AFYGR
‹1?
8.2- Was this hr
8,760?
4Y.1-Raise a blue flag to indicate excess new capacity and document AFYGrowth
4N.1/4.2-Assign total proxy
gen. to new units (adjusted when proxy gen. > future proj. gen.)
3.5aY.1-Note the capacity needed for GDU creation later
5-Multiply the BY
operational input/output
of each existing unit by AFYGR
6-Annual or hourly capacity or hour cap of any unit been reached?
7-Set the utilization of any
unit exceeding its capacity
back to the maximum allowed
Y
8-Calculate ExGen pool for hour: total gen. (incl. transfers) for this hour that exceeded the capacity of each unit
N
N
Y
8.1-Note potential capacity lacking to allocate excess generation for GDU creation
Y
N

## Slide 5
5
9aN-Go
to next page: ExGen pool Dist
From previous page
Y
9a-
More demand transferred that projected generation in any hour?
N
N
9Y.1- Log all hours in deficit review file, include calculations of lacking generation
9aY-Send up red flag
9Y.2- Insert generation deficit unit(s) in UAF and calculate unit data, including optimal load threshold, max_ annual_ERTAC_UF, & hourly proxy gen.
9Y.3- Re calculate the unit allocation order with the new generation deficit unit(s)
9-
Is capacity needed from earlier flags?
Creation of generation deficit units, if needed. New units inserted into the hierarchy. Run by fuel/unit type and region. Order of regions run may be important for future iterations of the model.
Y
STOP Tool: Start the QA Process
Go
to prev page: Box 2

## Slide 6
11-For first unit in allocation listing,
allocate utilization of that unit
from the ExGenPool
12-Has the unit
optimal threshold, annual capacity, op hour limit
of that unit
been reached?
12N.2-Go to next hr (10.5)
N
Y
ExGen Pool Distribution: This routine is done for hours where there is an ExGen pool. Continues the generation allocation to units. If the option is included to estimate energy transfer between regions, this would be done for primary and secondary consuming regions.
12N-Has hr
8,760 been
reached?
12N.1-Go to
spinning reserve page
N
Y
The current setup distributes the ExGenPool in 2 passes as shown on next page. Future iterations may want to distribute the ExGenPool in up to 5 passes.
10-Previous page: ExGen pool creation
10.5-Begin at the first/next hour in the hour-of-year hierarchy
12Y-Go to next page: double loop distribution
At this point, the program has distributed every hour’s ExGenPool for every fuel unit type in a region and must begin the spinning reserve test.

## Slide 7
13-Go to next unit on
allocation hierarchy
14-Any
units
left?
14Y.1-Allot utilization to the next unit on the allocation listing
14Y.2-Has the unit
optimal threshold, annual capacity, op hour limit
of that unit
been reached?
14Y.3-Has hr
8,760 been
reached?
14Y.3N-
Go to
next
hr (10.5)
N
N
N
Y
Y
Y
14Y.3Y-Go to
spinning reserve test
15-For first unit in allocation listing, allocate utilization
of that unit from the ExGenPool
16-Has any max capacity or annual UF or hours of op limit of that unit been reached?
17-Go to next unit on
allocation hierarchy
18-Any
units
left?
18Y.1-Allot utilization to the next unit
on the allocation listing
N
16N.1-Hr 8760 been
reached?
16N.1Y-Go to
spinning reserve test
N
Y
From 12Y:
Y
N
Y
ExGenPool Distribution: two loops

## Slide 8
Spinning Reserve: Checks to ensure that spinning reserve requirements for each region of the system are met. This portion of the work is performed after power distribution and ExGen pool distribution have been performed for all three fuels (coal, oil, natural gas). Spinning reserve for any hour can be satisfied by any extra capacity in any fuel type. The amount needed is calculated by finding the maximum capacity of the largest single unit running in any hour using any fuel and multiplying by 100%.
20-For each hour,
determine the capacity
of the largest unit operating
21-The required reserve capacity
equals 100% of the capacity
of the largest unit operating
23-Enough reserve
capacity exist in that hour?
22-Beginning at the first hour
in the hour of year hierarchy,
compare the required
reserve capacity to the amount of generation in the system, including transfers
not being used.
23Y-Hr 8760 reached?
24-Go
to
next
hour
(23)
Y
N
N
Y
25-Go to
next page: Emissions Check
23N-Send up red flag : more cap needed
23Y1-Print out a useful report detailing all reserve capacity needed.
23.5Y1-Output a database of hourly generation/heat input data for each unit as well as a summary table of unit generation/heat input (base yr versus future yr)
19.5-Print out a useful generation report by unit for stakeholder review
19.1-If any hour showed a demand generation deficit, print out a useful report showing where, when, how much, and for new generic unit creation, data on those units.
19 From previous pages

## Slide 9
Emissions Check: This part of the work checks to see if the expected controls, new generation, future year generation, and other system changes allow the universe of units to compare emissions against the various environmental caps.
25-
From spinning reserve page
26-For each hour of the year, for each unit, calculate emissions of
NOx and SO2 using the specific averaging method assigned to the fuel/unit type bin.
26.5-Apply unit level controls for units where future retrofits are expected to occur, based on information provided by States in the controls file and seasonal controls file and flag
28-Print out a useful report for the SIPs. Reports need significant detail to allow review of the results from application of transport and other state caps.
STOP Tool: Start the QA Process

## Slide 10
Decision 27 Explanation: This section checks to see if the emissions from the universe of EGUs may comply with the Transport Rule and other requirements
27.1a- For each state, calculate annual NOx, annual SO2, and ozone season NOx in the future year.
27.1b-Compare each state’s future year emissions totals to the totals for OS NOx, Annual NOx, and Annual SO2 listed in the State Total Listing.
State totals could be assurance levels, budget levels from CSAPR, or other appropriate state budgets; only for states subject to a state cap requirement.
State/Group
Cap Requirements
From Emissions Check
27.2a-Compare each group of state’s future year emissions totals to the applicable totals for that year for OS NOx, Annual NOx, and Annual SO2 listed in the Group Total Listing. Provide a report showing the comparison
There are as many groups as need to be defined for each pollutant: annual SO2 and NOx, OS NOx. The listing must delineate both the group total emissions for each pollutant and the states included in each group.
28- Goes back to the emissions check page